## Slide 1
Presented by : S.A.Eshtehardian
October 2020
Hardware requirements for training a deep neural network

## Slide 2: Table of contents
Introduction to CPU
Introduction to GPU
What is cuda?
Introduction to TPU
TPU’s internal architecture
A comparison between CPU, GPU and TPU
Google’s cloud TPU and GPU
Getting started with Cuda in pytorch
Getting started with activating TPU in pytorch

## Slide 3: Introduction to CPU
The term CPU stands for Central Processing Unit of a computer, which usually consists of more than one core, some of the cores may be virtual. The cores can be paralleled.

## Slide 4: Introduction to GPU
The term GPU stems from Graphics Processing Unit, which consists of more than a thousands of cores, making it a perfects choice for parallel computing.

## Slide 5
What is cuda?
Cuda is a parallel computing platform that makes it easier to use GPU for different goals with various programming languages.

## Slide 6: Introduction to TPU
The term TPU stems from Tensor Processing Unit, which has been defined as a hardware in order to make the parallel processing easier for problems including linear algebra( i.e. Deep Learning, Image Processing). They are first designed specifically for Google’s TensorFlow framework.

## Slide 7
TPU’s internal architecture
Tensor Processing Unit (TPU), a custom ASIC, built specifically for machine learning — and tailored for TensorFlow, can handle massive multiplications and additions for neural networks, at great speeds while reducing the use of too much power and floor space. A typical cloud TPU has two systolic arrays of size 128 x 128, aggregating 32,768 ALUs (Arithmetic Logic Units) for 16-bit floating-point values in a single processor. Thousands of multipliers and adders are connected to each other directly to form a large physical matrix of operators, which forms a systolic array architecture as discussed above.

## Slide 8
It consists of four independent chips. Each chip consists of two calculation cores, called Tensor Cores, which include scalar, vector and matrix units (MXUs). In addition, each Tensor Core, with 8 GB chip memory (HBM), has been unified. Each of the 8 cores on the TPU can execute user accounts (XLA ops) independently. High-bandwidth interconnection paths allow the chips to communicate directly with each other.
TPU’s internal architecture

## Slide 9
A comparison between CPU, GPU and TPU

## Slide 10: Google’s Cloud TPU and GPU

## Slide 11: Getting started with cuda in pytorch

## Slide 12
Getting started with activating TPU in pytorch